# JIRA Scripts
The scripts in:
/usr/local/devel/VIRIFX/software/SampleTracking

provide a command line interface to the JIRA sample tracking system. They can perform various actions on multiple samples at a time.
## Selecting Samples
The samples that are acted on can be selected either by Database and Lot ID or using a Tuple file.
### By Lot ID
Format: --lot <lot ID>, or -l <lot ID>
Example: --lot ED01
Description:
This is the default form of selection. It is used unless the --file parameter is set.
The Lot ID can either be passed to the program using the --lot parameter or entered when the program is run.
Actions:
- This method of selection can be used with all but Sub-Task-assign.
- However it may not be appropriate when moving samples between steps. If any of the samples are at a different step then they may fail to move.
Selects:
- JIRA Sample creation; all of the samples from the lot that are not already associated with a JIRA Sample are used
- All other actions; all of the samples from the Lot that are already associated with a JIRA Sample are used
Notes:
A database must also be specified if a Lot ID is used. This can be set via the --database parameter or entered when the program is run.

### Using a Tuple file
Format: --file <filename>, or -f <filename>
Example: --file example.csv
Description:
Files can only be specified using the file parameter. The file format should be:
(<db>,<collection code>,<bac id>)+
There is no header. The lines contains a combination of Database, Collection code and BAC ID that uniquely identifies the sample to process and where to find it in the GLK.
Actions:
This method of selection can be used with all of the actions.
Selects:
A sample for each of the lines that contains a BAC ID that is valid in the specified database and identifies a sample that already has an associated JIRA Sample.
Note:
- The samples may not be acted on in the same order that they appear in the tuple file.
- Multiple databases can be used in the same tuple file
- The Collection code is currently ignored by all the Sample tracking scripts.
## Selecting Sub-tasks
Format: --subtask "<sub-task's name>", or -s "<sub-task's name>"
Example: --subtask "PCR Task"
Description:
Sub-tasks are selected using a combination of a Tuple File and the name of the type of sub-task to select.
The sub-task can be defined on the command-line as shown above or it can be entered when prompted. Actions:
This method of selection can be used with all of the actions.
Selects:
A sub-task for each of the samples selected using the Tuple file.
Notes:
- The sub-task name is case insensitive.
- This should only be used with the commands that start with 'subtask-'
- Selecting the samples using database and lot is not currently possible
## Script Parameters
All of the scripts share the following parameters:
-c,	--comment="<comment>"	The comment to add to the sample/Sub-Task's log
-d,	--database="<db>"	The GLK database the lot is stored in [e.g. giv]
-f,	--file="<full filename>"	A tuple file listing the samples to act on
-l,	--lot="<lot id>"	The lot to import [e.g. RFH301]
-t,	--test	No changes are made to JIRA or the GLK
-h,	--help	Display this message
If a required parameter is not specified, using one of these attributes, then a prompt will request the value.
## Commands acting on Samples
For all of the examples, in the 'Commands acting on Samples' and 'Commands acting on Sub-tasks' sections, the file example.csv contains:
giv2,BUCB,38354
giv2,BUCB,38355
### Sample Creation
Command: sample-create.sh
Description:
Creates a group of new JIRA Samples and links them to the GLK
Example:
(User input is italicized in the examples below)
bash-3.2$ ./sample-create.sh
Selecting Samples based on Lot ID.
Please enter DB to use
giv
Please enter lot code to use
EH03
Database: giv
Lot: EH03
Please enter a comment
Test Comment
Carrying out 9 actions
### Assigning Samples
Command: sample-assign.sh
Description:
Assigns a group of JIRA Samples to a single user
Example:
bash-3.2$ ./sample-assign.sh
Please enter the JIRA username to use
pedworth
Please enter the JIRA user's password to use
Selecting Samples based on Lot ID. To use a tuple file add
--file=<filename> to the command
Please enter DB to use
giv
Please enter lot code to use
rfh301
Using password from ~/.sqshrc
Please enter the user to assign the samples/subtasks to
pedworth
Please enter a comment
Assigning the samples
Carrying out 273 actions

Asignee: is the username used, by the person the task is being assigned to, when logging into the system
### Moving Samples
Command: sample-move.sh
Description:
Moves a group of JIRA Samples between steps
Example:
./sample-move.sh --file example.csv
Please enter the JIRA username to use
pedworth
Please enter the JIRA user's password to use
Selecting Samples based on file example.csv.
Using password from ~/.sqshrc
Searching for Available Steps
Available Steps:
9400,"Move"
9310,"Deprecate"
9300,"Unresolved"
9095,"Deliver Data"
Please enter step to move samples to (number or name)
9095
Please enter a comment

Carrying out 2 actions

Comment can be left blank with any of the scripts (except sample-comment) if no comment is desired.

### Commenting on Samples
Command: sample-comment.sh
Description:
Adds a Comment to the JIRA Samples without carrying out any modification to the Samples.
Example:
./sample-comment.sh --database giv --lot rfh301 --user pedworth
Please enter the JIRA user's password to use
Selecting Samples based on Lot ID. To use a tuple file add
--file=<filename> to the command
Using password from ~/.sqshrc
Please enter a comment
this is a new comment
Carrying out 273 actions
## Commands acting on Sub-tasks
### Creating Sub-tasks
Command: subtask-create.sh
Description:
Creates a new Sub-task for each JIRA Sample specified
Example:
TODO
### Assigning Sub-tasks
Command: subtask-assign.sh
Action Name: assign
If jira-cmd.sh is called with the subtask option set then the commands will be applied to a set of subtasks instead of samples. The commands remain the same.
Description:
This behaves the same as the sample-assign.sh script with the exception that a Sub-task is required. The action takes place on the Sub-tasks of the JIRA Samples specified. The Sub-tasks are filtered to only include a single type using the --subtype/-s attribute or the value provided when prompted.
Note:
There may be more than one Sub-task of a specific type associated with a single JIRA Sample; currently there is no way to distinguish between these Sub-tasks and both will have their assignee set by this script.
Note:
This command currently only works with Tuple files. Selecting the samples using Database and Lot ID is not supported.
Example:
./subtask-assign.sh --user pedworth --file example.csv --assignee pedworth
Please enter the JIRA user's password to use
Please enter the type of sub-task to act on
PCR Task
Please enter a comment
assigning using the commandline flags
Carrying out 2 actions
### Moving Sub-tasks
Command: subtask-move.sh
Action Name: move
Description:
Moves a group of JIRA Sample's sub-tasks between steps
Example:
 ./subtask-move.sh --file example.csv --user pedworth --comment "using a command-line comment"
Please enter the JIRA user's password to use
Please enter the type of sub-task to act on
pcr task
Searching for Available Steps
Available Steps:
99,"Fail, move to [Failed]"
98,"Return to Previous Step [Open]"
Please enter step to move samples to (number or name)
98
Carrying out 2 actions
### Commenting on Sub-tasks
Command: subtask-comment.sh
Action Name: N/A
Description:
Adds a Comment to the JIRA Sample's sub-tasks.
Example:
./subtask-comment.sh --file example.csv --subtask "pcr task"
Please enter the JIRA username to use
pedworth
Please enter the JIRA user's password to use
Please enter a comment
This is a subtask comment
Carrying out 2 actions
## Combining actions
Format: jira-cmd.sh --action "action1 action2 action3"
Description:
This program allow multiple actions to be combined and carried out on the selected set of JIRA Samples. The selection of the samples is exactly the same as with all the other programs. Sub-tasks can be selected by including the --subtask argument. The selection of the actions is done by the required parameters 'action'. This is followed by a list of actions separated by spaces and surrounded by quotes.
Valid actions:
    assign	see Assigning Samples
    create	see Sample Creation
    move	see Moving Samples
    subtask	see Creating Sub-Tasks
Example:
jira-cmd.sh --action "assign move" -f example.csv
./jira-cmd.sh --action "assign move" -f example.csv
Please enter the JIRA username to use
pedworth
Please enter the JIRA user's password to use
Selecting Samples based on file example.csv.
Using password from ~/.sqshrc
Please enter the user to assign the samples/subtasks to
pedworth
Please enter a comment
comment 1
Carrying out 2 actions
Selecting Samples based on file example.csv.
Searching for Available Steps
Available Steps:
9400,"Move"
9310,"Deprecate"
9300,"Unresolved"
9095,"Deliver Data"
Please enter step to move samples to (number or name)
9095
Please enter a comment
comment 2
Carrying out 2 actions

Notes:
- The user name and password are only prompted for once
- A separate comment is prompted for each action. To add only one comment to the Samples enter blank comments after the first one.
- If a comment is provided on the command-line it will be added when the first action takes place. Comment prompts will appear for the later actions.